## Slide 1
Asymmetric VLAN with DAP

## Slide 2: Asymmetric VLAN
Defining Asymmetric VLAN
  The device configuration allows a port to be defined as an untagged member only in one VLAN and tagged in multiple VLANs. By enabling Asymmetric VLAN on the device, a port is defined as an untagged member in multiple VLANs.
Sever
VLAN 1
Private
VLAN 10
Public
VLAN 20
VLAN 1

## Slide 3: Asymmetric VLAN
Asymmetric VLAN Layer 2 Application.
  To share the server resource(file server, mail server…) for multi group (VLAN), but each group cannot access each other.
Sever
VLAN 1
Private
VLAN 10
Public
VLAN 20
VLAN 1
  VLAN 10 and VLAN 20 both can access the VLAN 1
  VLAN 10 and VLAN 20 cannot access each other

## Slide 4: Scenario

## Slide 5: Asymmetric VLAN with DAP
Asymmetric VLAN Application.
  VLAN 10 and VLAN 20 both can access the VLAN 1
  VLAN 10 and VLAN 20 cannot access each other
Private
VLAN 10
Public
VLAN 20
Sever
VLAN 1
PC 1
PC 2
Private
VLAN 10
Public
VLAN 20
VLAN 1

## Slide 6: Configuration

## Slide 7: Asymmetric VLAN with DAP
Using DGS-1210-48 to create VLAN 1, VLAN 10 and VLAN 20, and asymmetric VLAN enabled.
  VLAN 10 and VLAN 20 both can access the VLAN 1, and it own VALN
  VLAN 10 and VLAN 20 both cannot access each other
Private
VLAN 10
Public
VLAN 20
Sever
VLAN 1
Sever connect to Port 13
AP connect to Port 15
PC 1
PC 2
Private
VLAN 10
Public
VLAN 20
VLAN 1

## Slide 8: Switch configuration
DGS-1210-48 configuration
  VLAN 10 : port 1~5, and 11~15, port 15 with tag
  VLAN 20 : port 6~10, and 11~15, port 15 with tag
  VLAN 1 : port 1~48, port 15 with tag

## Slide 9: DAP configuration
DAP-2360 configuration
  VLAN 10 : S-1, ethernet port with tag
  VLAN 20 : S-2, ethernet port with tag
  VLAN 1 : Mgmt, LAN, S-1, S-2, ethernet port with tag
Index | SSID | Band | Encryption | Delete | 
Primary SSID | dlink | 2.4 GHz | None | 
Multi-SSID1 | privada-1 | 2.4 GHz | None | 
Multi-SSID2 | publica-1 | 2.4 GHz | None | 

## Slide 10: Verifying

## Slide 11: Asymmetric VLAN with DAP
Testing results,
  PC 1 can access the Server VLAN 1 and the computers under VLAN 10, but not the computers under VALN 20
  PC 2 can access the Server VLAN 1 and the computers under VLAN 20, but not the computers under VALN 10
Private
VLAN 10
Public
VLAN 20
Sever
VLAN 1
Sever connect to Port 13
AP connect to Port 15
PC 1
PC 2
Private
VLAN 10
Public
VLAN 20
VLAN 1

## Slide 12: Asymmetric VLAN with DAP
Testing results,
  PC 1 ping to Sever and VLAN 10 PC with VLAN tag 10, sniffer from LAN of AP
Private
VLAN 10
Public
VLAN 20
Sever
192.168.0.88
VLAN 1
Sever connect to Port 13
AP connect to Port 15
PC 1
192.168.0.44
PC 2
192.168.0.55
Public
VLAN 20
VLAN 1
Private
VLAN 10

## Slide 13: Asymmetric VLAN with DAP
Testing results,
  Sever reply the ping to PC1 with VLAN tag 1, sniffer from LAN of AP
Private
VLAN 10
Public
VLAN 20
Sever
192.168.0.88
VLAN 1
Sever connect to Port 13
AP connect to Port 15
PC 1
192.168.0.44
PC 2
192.168.0.55
Public
VLAN 20
VLAN 1
Private
VLAN 10

## Slide 14: Asymmetric VLAN with DAP
Testing results,
  VLAN 10 PC reply the ping to PC1 with VLAN tag 10, sniffer from LAN of AP
Private
VLAN 10
Public
VLAN 20
Sever
192.168.0.88
VLAN 1
Sever connect to Port 13
AP connect to Port 15
PC 1
192.168.0.44
PC 2
192.168.0.55
Public
VLAN 20
VLAN 1
Private
VLAN 10

## Slide 15: Asymmetric VLAN with DAP
Testing results,
  PC 2 ping to Sever and VLAN 20 PCs with VLAN tag 20, sniffer from LAN of AP
Private
VLAN 10
Public
VLAN 20
Sever
192.168.0.88
VLAN 1
Sever connect to Port 13
AP connect to Port 15
PC 1
192.168.0.44
PC 2
192.168.0.55
Public
VLAN 20
VLAN 1
Private
VLAN 10

## Slide 16: Asymmetric VLAN with DAP
Testing results,
  Server reply ping to PC 2 with VLAN tag 1, sniffer from LAN of AP
Private
VLAN 10
Public
VLAN 20
Sever
192.168.0.88
VLAN 1
Sever connect to Port 13
AP connect to Port 15
PC 1
192.168.0.44
PC 2
192.168.0.55
Public
VLAN 20
VLAN 1
Private
VLAN 10

## Slide 17: Asymmetric VLAN with DAP
Testing results,
  VLAN 20 PC reply ping to PC 2 with VLAN tag 20, sniffer from LAN of AP
Private
VLAN 10
Public
VLAN 20
Sever
192.168.0.88
VLAN 1
Sever connect to Port 13
AP connect to Port 15
PC 1
192.168.0.44
PC 2
192.168.0.55
Public
VLAN 20
VLAN 1
Private
VLAN 10

## Slide 18
Reference

## Slide 19
Case reference,
  DLA20130606000001
  HQ20130614000003
  HQ20130618000006
  HQ20130704000009